## Slide 1: Theory of narrow-band mode-locking
厦门大学：罗塞雨
导师：蔡志平教授

## Slide 2: Abstract
It should be emphasized that the mode locking of lasers can be thought as two types of balance: The balance between pulse broadening and pulse shortening; the balance between the phase shift by GVD and one by nonlinearity (self-phase modulation).
If the former balance is not obtained, the mode locking pulses will not occur; if only the former balance is obtained, the mode-locking pulses can occur but will be unstable; if both balances are obtained, the stable mode locking pulse will occur.

## Slide 3: Abstract
Basically, Stark effect makes multiple longitudinal modes oscillating simultaneously become possible.
What’s more， gain-line splitting (Stark splitting) induced by an intra-cavity laser field can form a dip or dips in gain-line shape, with which a balance between pulse broadening and pulse shortening can be achieved. That is to say, the first balance is obtained and the gain medium with such a gain-line shape can produce short pulses. [1986, J. J. Sanchez-Mondragon]
Since the Stark splitting is symmetric, there is no additional group-velocity dispersion (GVD). The SML pulses without dispersion compensation will occur in those lasers whose gain media have a dip in the gain-line shape, if the nonlinearity and GVD of the host materials can be neglected.
[1986, J. J. Sanchez-Mondragon]. “Pulse compression caused by a spectral hole in an inhomogeneously broadened line of an amplifier”, Centro de Investigaciones en Optica, A. C., Apdo. Postal 948, Leon, Gto. 37000, Mexico

## Slide 4: Abstract
Narrow gain width makes mode-locking easier (so it can start mode-locking by itself): stronger intra-cavity laser field owing to larger gain can generate frequency shift of the Stark splitting, which is beneficial to mode-locking.
Since the gain width is small, the allowed oscillation frequencies are limited, which means less longitudinal laser modes would anticipate in mode-locking, leading to a possibly less stable mode-locking state with a larger pulse width in the time domain compared with that of large gain width laser gain material.

## Slide 5: Abstract
By increasing the laser cavity length, thus reducing the fundamental frequency of the cavity, more stable mode-locking lasers could be attained with shorter pulse width in the time domain.
The above statement is true on condition that the pulses would be sustained in the extended long laser cavity. Fortunately, that is true for our Pr:YLF solid-state laser. The extended laser cavity is in the air, there should be no phase shift by GVD or by nonlinearity (self-phase modulation).

## Slide 6: 1. Mode-Locking Theory
a laser can oscillate at a number of resonant frequencies whose spacing is equal to the fundamental frequency ωR of the cavity:
The output electric field of the generated lightwave in the temporal domain is the summation of all the oscillating modes given as

## Slide 7
when the modes are forced to lock together, that means all the N modes are either in phase or different in a multiple number of 2π, En
and Φn will be constants. The simplest case is when En = 1, and Φn = 0
which is an oscillation at frequency ω0 modulated with the sinc envelope function. The average power is thus given by

## Slide 8
The periodic train of pulses that have the following properties
the pulse period is T = 2π/ωR;
the peak power is N times the average power;
the peak field amplitude is N times the amplitude of a single mode;
the pulse width, defined as the time from the peak to the first zero, is τ =T/N, which shortens as N increases.

## Slide 9
Note that the Fourier transform is imaginary
Appendix: Fourier Transform

## Slide 10
Graphical development of the Fourier transform of a sequence of equal distant impulse function

## Slide 12
Fourier transform of a square wave function (Fourier series)

## Slide 13
Fourier transform of a pulse waveform

## Slide 14
Lorentzian line shape
Gaussian line shape

## Slide 15: Frequency Convolution Theorem

## Slide 16: Graphical derivation of the sampling theorem

## Slide 17: 5. The Discrete Fourier Transform
aliasing
rippling
Note that sampling in the time/frequency domain resulted in a periodic function of frequency/time;
N time samples and N frequency values represent one period of the time and frequency domain waveforms, respectively.
Time domain sampling
Truncation
Frequency domain
sampling

## Slide 18: 2. Mode-Locking Techniques
2.1 Passive Mode Locking
Passive mode locking technique refers to those locking without any external
radio frequency (RF) signal for seeding. The pulses are formed passively
through the internal structure of the laser that gives more advantages (less
loss, high gain) to signal if it travels in the pulse form rather than in a CW. The simplest method is to insert a saturable absorber into the cavity. The saturable absorber is a nonlinear optical component whose absorption coefficient decreases when the optical intensity increases.
Thus, the pulse train with high peak intensity would pass through the
absorber with much less loss as compared to that in a CW laser with several
modes as the energy available is concentrated in the periodic pulses, thus a
stable pulse train can be formed in the cavity.
2.1.1 Using saturable absorber

## Slide 19
Schematic of a passive MLL integrated with a saturable absorber in the cavity

## Slide 20
Instead of using the saturable absorber, a nonlinear polarization rotation
(NPR) technique can be used for passive mode locking, as shown in the
Figure below. In this system, a nonlinear phase shift is imposed on the signal
with high peak power and thus rotates its polarization state to align with the
analyzer axis. The signal thus passes through the analyzer with minimum
loss. On the other hand, the CW signal with a low average power experiences
zero nonlinear phase shift and thus its polarization state is not rotated
to align with the analyzer axis. It is then blocked by the analyzer. Therefore,
pulses with high peak power are formed in the cavity instead of the CW
with a low average power.
2.1.2 Using polarization rotation technique

## Slide 21
Schematic of an NPR passive MLFL

## Slide 22
A passive mode-locked laser (MLL) has the potential to produce a very
short laser pulse, down to femtoseconds. The shortest pulse generated in the communication wavelength window to date is 5 fs?
Moreover, passive mode-locking is a self-locking phenomenon, it means that the pulse is formed without any external modulating signal.
However, the spacing between two pulses is varied from pulse to pulse since there is no control mechanism to force the pulses to be equally spaced. This is the disadvantage that makes passive MLLs not suitable for high-speed optical transmission systems, in which precise timing from pulse to pulse is required.
2.1.3 Advantages and Disadvantages of Passive MML

## Slide 23
2.2.1 Active Mode Locking by Amplitude Modulation
In actively MLLs, mode locking can be induced either by amplitude modulation (AM), phase modulation (PM), or frequency modulation (FM). When amplitude is modulated by an external RF signal with a frequency of fm, the oscillating mode at the optical frequency f0 shades its energy to the two side bands located at f0+fm and f0-fm, as shown in the Figure below. If the modulating frequency fm is chosen so that fm=fR, the side bands are coincident with the adjacent modes of the laser and hence the energy from ith mode is transferred to its adjacent (i+1)th and (i−1)th modes. In other words, the energies of the modes in the laser are transferred from one to the other. This causes the phase of the modes locked together and hence a mode-locked pulse train is formed.

## Slide 25
In actively MLLs, mode locking is induced by modulating the gain or loss
of the cavity with an external signal at the fundamental frequency fR.
A common method of active mode locking is inserting an acousto-optic
modulator (AOM) into the cavity, as shown in the Figure below. This is the first
method used in the experiment for the observation of mode-locked pulses in a helium–neon laser. The AOM is used to deflect light energy from the cavity by varying the refractive index of the medium in a standing wave profile. Thus, the undeflected beam is amplitude modulated.
AOM is widely used in several MLLs as it offers a very low insertion loss. However, the operating frequency of the AOM is limited and far below the pulse rate required for modern optical communication, typically, from a few hundred megahertz to a few gigahertz depending on the acoustic velocity of the acousto-optic material.

## Slide 26
Due to the limited bandwidth of AOMs, they are normally replaced by LiNbO3 (铌酸锂)intensity or phase modulators whose bandwidth may reach 40 GHz or higher in high repetition rate actively MLLs.
In addition, all-fiber cavity is also used in those lasers to take advantage of fiber lasers such as low threshold, single mode, and high beam quality. Moreover, high optical intensity in a small cross section of the fiber enables one to obtain nonlinear effects for short pulses with even a low pump power.
Another method of mode locking is to modulate the gain of the amplifying medium as in Refs. [?,?]. In those experiments, the gain of the semiconductor amplifier is modulated by an external modulating signal. The lightwaves therefore experience a periodical gain and form the mode-locked pulses in the cavity. A semiconductor laser has the potential to generate very short pulses due to its wide spectral gain region.

## Slide 27
2.2.2 Stimulation of Active Mode Locking by Amplitude Modulation
Pulse generation
Spectrum

## Slide 28
Spectrum without AM
Pulse generation without AM
Without AM, mode locking will not be stable

## Slide 29
Pulse generation without frequency filter
Spectrum without frequency filter
In a mode-locked fiber ring laser (MLFRL),
Without frequency filter, high frequency noise would deform the laser pulses

## Slide 30
Self-Mode-Locking
0.3 m cavity

## Slide 31
Kerr mode-locking
1.8 m cavity

## Slide 33
Green Self-mode-locking

## Slide 37
谢谢！